Call Mr Robeson LX Cue List.

Basic Minimum (With Specials)

July 2015

Warm Wash

Cool Wash

Specials in order of necessity (See focus notes and plan to identify numbers, focus etc.):

17: Piano Key Board (PKB)

15: Chair Special. L153. Source 4/Profile. Focussed on chair.

18: Stage Left Special. Open White. Source 4/Profile Focussed DSL

24: Center Stage Special: L121. Fresnel or large profile

22: Deep Night Wash: L079. General Wash

13: Down Stage Centre Special. Open white Source 4/Profile

-------------------------- Above this line most essential. Below, very desirable-------------------------

6: Exit Special: R317 Profile or Barn doored Fresnel at head height in USL wings

23: Street light. L441x2 Fresnel, Centre and DSL

8: Break up gobo

16: Window gobo

5: Entrance Special: L200 fresnel.

25: Piano 1: L103 or warm. Profile focused on piano and pianist (note: from SL)

14: Piano 2: L201 or cool. General wash in direction of piano

31: Picture: Profile shuttered to photo on/near piano

Others as units available: 26, 27, 28, 29

| Page | LX Cue | Description | Time Up/Dn | Channels Used |
| --- | --- | --- | --- | --- |
| 2 | 0.5 | Preset |  | Warm @30 HL @ 50. Piano 1 @ 25. PKB @ 25 |
| 2 | 1 | Houselights and Pre-Set out | 12 |  |
| 2 | 1.5 | Entrance | 12 | Cool wash @ 20 (or Entrance Special @ 60). PKB @ 25 |
| 2 | 2 | Entrance. | 12 | Cool wash @ 50. (or entrance) Break up gobo @ 50 (or cool @ 30). PKB @ 25 |
| 2 | 3 | Show wash Up | 5 | Warm @ 50 Cool @ 50. PKB @ 25 Break up @ 50 |
| 2 | 4 | Brighter Gen. | 3 | Warm @ 70 Cool @ 70 PKB @ 25 |
| 3 | 5 | Warm Wash | 30 | Warm @ 100 PKB @ 25 |
| 6 | 6 | Dim, add piano | 5 | Warm @ 30 Centre Chair Special @ 70 PKB @ 25. Piano 1 @ 30 |
| 6 | 7 | Warm Wash | 7 | Warm @ 100. PKB @ 25 |

| Page | LX Cue | Description | Time Up/Dn | Channels (Change) |
| --- | --- | --- | --- | --- |
| 7 | 8 | Outside | 5 | Warm @ 30 (SL only) or Street light @ 50 Night wash @ 50. PKB @ 25 |
| 8 | 9 | Theatre (speaking on podium) | 3 | Stage Left Special @ 100 PKB @ 25 |
| 8 | 10 | Warm Wash As Q 7 | 5 | As Q 7 |
| 10 | 11 | Theatre (singing DS) | 3 | DSC Special @ 100 PKB @ 25. Piano 1 @ 30 |
| 11 | 12 | Add Warm | 3 | DSC Special @ 100 Warm @ 60. PKB @ 25. Piano 1 @ 30 |
| 12 | 13 | Theatre (As 11) | 3 | DSC Special @ 100 PKB @ 25. Piano 1 @ 30 |
| 13 | 14 | Show wash | 2 | As Q 7 |
| 15 | 15 | Cool | 8 | Warm @ 30 Cool @ 80. PKB @ 25 |
| 15 | 16 | Brightens | 3 | Warm @ 60 Cool @ 80. PKB @ 25 |
| 15 | 17 | Theatre (Speaking) As Q 9 | 3 | Stage Left Special @ 100 PKB @ 25 |
| 16 | 18 | Show Wash As Q 10 | 2 | As Q 7 |
| 16 | 19 | Cool Wash (Reporters) | 5 | Cool @ F DSC Special @ 60 PKB @ 25 |
| 17 | 20 | Warm Wash (As Q 18) | 2 | As Q 7 |
| 17 | 21 | Cool Wash As Q19 | 2 | As Q 19 |
| 17 | 21.5 | Warm Wash (As Q 20) | 2 | As Q 7 |
| 19 | 22 | External Wash | 2 | Warm Wash @ 100 Cool Wash @ 100 PKB @ 25 |
| 19 | 23 | Warm Wash (As Q 20) | 2 | As Q 7 |
| 19 | 24 | External Performance Wash | 2 | Warm Wash @ 100 Cool Wash @ 100. PKB @ 25 Stage Left Special @ 100 PKB @ 25 |
| 21 | 25 | Warm Wash (As Q 20) | 2 | As Q 7 |
| 21 | 26 | External Performance Wash | 2 | Warm Wash @ 100 Cool Wash @ 100. PKB @ 25 Stage Left Special @ 100 |

| Page | LX Cue | Description | Time Up/Dn | Channels (Change) |
| --- | --- | --- | --- | --- |
| 23 | 27 | Darken surround | 5 | Warm Wash @ 30 Cool Wash @ 30. PKB @ 25 Stage Left/DSC Special @ 100 |
| 23 | 28 | Warm Wash. As Q21.5 | 3 | As Q 7 |
| 24 | 28.5 | Warm wash, add cool | 10/15 | Warm Wash @ 100 Cool Wash @ 60 PKB @ 25 |
| 26 | 29 | State darkens, add special | 15/20 | Warm Wash @ 60 Cool Wash (or break up)@ 60. PKB @ 25 Center Stage Special @ 40 |
| 26 | 30 | Dark. | 2 | Center Stage Special @ 100 Break up @ 70 PKB @ 25 |
| 26 | 31 | Darkens. | 5 | Center Stage Special @ 70 Break up @ 70 PKB @ 25 |
| 27 | 32 | Slowly Darkens more. | 70 (seventy) | Center Stage Special @ 15 Break up @ 30 PKB @ 25 |
| 27 | 33 | Warm Wash. (As Cue 10) | 0.1 | As Q 7 |
| 28 | 34 | Committee Wash | 4 | Cool Wash @ 80 PKB @ 25 |
| 28 | 35 | Interrogation Special | 5 | Center Chair Special @ F Window gobo @ F PKB @ 25 |
| 29 | 36 | Committee Wash | 4 | Cool Wash @ 80 PKB @ 25 Window gobo @ F |
| 29 | 36.5 | Interrogation special | 4 | Center Chair Special @ F Window gobo @ F PKB @ 25 |
| 32 | 37 | Warm Wash | 5 | Warm Wash @ 80 PKB @ 25 |
| 32 | 38 | Brighten | 4 | Warm Wash @ 100. PKB @ 25 |
| 33 | 39 | Brighten, add DS special | 10 | Warm Wash @ 100 Cool Wash @ 50 DSC Special @ 50 PKB @ 25 |
| 34 | 39.5 | Brightens | 5 | Warm Wash @ 100 Cool Wash @ 100 DSC Special @ 80 PKB @ 25 |
| Page | LX Cue | Description | Time Up/Dn | Channels (Change) |
| 34 | 40 | Warm Special | 2/8 | Warm Wash @ 60. PKB @ 25 |
| 35 | 41 | Darkens, add night special | 5 | Warm @ 30 (SR only) Night Special @ 100 PKB @ 25 |
| 35 | 42 | Warm and Cool Wash | 5 | Warm Wash @ 100 Cool Wash @ 60 PKB @ 25 |
| 37 | 43 | Darkens | 5 | Warm @ 30 (SR only) Night Special @ 100 PKB @ 25 |
| 38 | 44 | Special | 5 | Street light @ 50 (or Warm @ 60, SL only) PKB @ 25 |
| 38 | 45 | Darkens As Q 43 | 5 | Warm @ 30 (SR only) Night Special @ 100 PKB @ 25 |
| 38 | 46 | Off stage exit special. | 6/15 | Exit Special (or Warm) @ 50 (SL only) PKB @ 25 |
| 38 | 47 | Blackout | 10 |  |
| 38 | 48 | Curtain call. | 2 | Warm @ 100 Cool @ 60. PKB @ 25 |
| Talkback. | 49 | Dim, Add H/L | 2 | Warm @ 80 HL @ 60. PKB @ 25 |